## Slide 1: 3D Numerical Ray Tracing for the APS-Upgrade Storage Ring Vacuum System Design
Jason Carter
Technical Lead, APS-U Storage Ring Vacuum System Design Group
Advanced Photon Source
Argonne National Laboratory, Lemont, IL
MEDSI 2018 Paris, France
June 28, 2018
Notes: Univ of Chicago Review, Aug. 30, 2010
1

## Slide 2: Agenda
APS Upgrade project
  Project and storage ring vacuum system overview
2D ray tracing
  Summary for APS-U
  Limits of analysis
3D ray tracing
  Motivations
  New MatLab program for APS-U: Algorithm, theory, model geometry
  Ray tracing results: thermal loads for ANSYS & informing beam position limits
BEAM
DIRECTION

## Slide 3: APS Upgrade Project - Overview
Advanced Photon Source (APS)
  7 GeV, 100 mA, 1.1 km circumference synchrotron light source built in 1995
APS-U multi-bend achromat lattice
  6 GeV, 200 mA beam current
  Optimized for brightness above 4 keV
  APS-U exceeds the capabilities of today’s storage rings by 2 to 3 orders of magnitude in brightness, coherent flux, and nano-focused flux
  5000 hrs / year of beam to users at 95% availability
  Anticipated operations ~2025
  Powers entire beamline suit to meet needs of APS’s >5000 users per year
  1 year APS down time (6-7 months installation)
APS-U
APS
APS today: double-bend lattice
APS-U: multi-bend lattice

## Slide 4: APS U Storage Ring Vacuum System - Overview
40x sectors, each ~27.6 meters in length
  22 m arc sections (our scope) + 5.6 m straight sections
Small aperture vacuum chambers between narrow magnet gaps
Hybrid vacuum system design
  Discrete pumping with ion pumps and lumped NEGs
  Distributed pumping with NEG strips and NEG coatings
Low pressure design target for good beam lifetimes
  2 nTorr @ 200 mA by 1000 A*hrs conditioning (1E-11 Torr/mA)
Existing APS storage ring chamber compared to new 22 mm ID APS-U style chamber
Beam Direction
QUAD
DOUBLET
QUAD
DOUBLET
L-BEND
L-BEND
L-BEND
L-BEND
STRAIGHT
MULTIPLET
STRAIGHT
MULTIPLET
FODO SECTION

## Slide 5: Top view ray tracing w/ 2D CAD
Conventional 2D ray tracing with a top view layout in AutoCAD
  For APS, 6x discrete photon absorbers take majority of unused photon heat load
Smaller scale apertures of next-gen machines make more components participate in ray trace
  For APS-U, 20x components including vacuum chambers participate in ray trace
Original APS storage ring vacuum system 2D ray trace using AutoCAD
Typical APS-U storage ring vacuum sequence: 22 mm ID chamber protecting downstream flange joint, inline absorber protecting length of downstream BPM
BEAM
DIRECTION

## Slide 6: Summary of APS-U storage ring ray tracing
2D Ray Tracing for APS-U
  Rays strike 20 separate vacuum components per sector and breakdown requires a complex 2D CAD layout
  14.3 kW generated per sector @ 200 mA
    5.3 kW on FODO section chambers
    3.5 kW on B-side crotch absorber
    600 W in B Quad Doublet
Ray tracing compared and verified using 3 separate tools:
  2D CAD layout
  SynRad, CERN’s 3D ray tracing code
  New 3D MatLab program for studying beam missteering
Summary of APS-U’s 2D ray trace
Beam Direction

## Slide 7: Motivations for 3D ray tracing
Difficult to ensure protection of new machines with small apertures, sensitive components, and more photon intercepting chambers and absorbers
Beam missteering happens in 3D and presents too large of a set of possibilities to capture in 2D
Absorbers and chambers need to be designed and analyzed to withstand worst-case radiation loads
How to reasonably specify limits for beam position limit detection systems?
Beam Direction
Typical APS-U vacuum sequence: Chamber protecting downstream flange joint, inline absorber protecting length of downstream BPM
BEAM
DIRECTION

## Slide 8: APS-U 3D ray tracing
Ray tracing compared with 3x separate tools:
  2D layout: takes time to create CAD layout and break down results, modify for scenario studies
  SynRad (CERN code): 3D models extracted from full vacuum system CAD assembly, quick to modify with practice, difficult to compare results across vacuum system
  Numerical 3D ray tracing with new MatLab code: explore beam
Better understanding of ray tracing and missteering helps ensure robust shielding within narrow apertures
Beam Direction
BEAM
DIRECTION
SynRad ray tracing (absorbers highlighted in red)
MatLab ray tracing
MatLab with beam missteering
BEAM
DIRECTION
A-MULTIPLET
A:M1
L-BEND
A:M2
L-BEND

## Slide 9: Overview of numerical ray tracing algorithm
BEAM
DIRECTION
2D ray tracing model in MatLab (E-beam bends in blue, photon ‘rays’ in green, strike points in red)
Build geometry based on sequentially ordered geometric elements along beam path
Generate tangential rays from points along bend path
  If no missteering: just one ray per point
  If yes missteering: at each point, generate numerous rays with deviated positions and angles based on local phase space ellipses
Find where ray strikes by checking downstream geometry sequentially
Record data from strike on element: strike coordinates, total heat (W), intensity (W/mm, W/mm2), etc.
Use logic to find ‘worst rays’ on each element after many possible strikes

## Slide 10: Overview of numerical ray tracing algorithm
BEAM
DIRECTION
Common synchrotron radiation heat load equations
Diagram of ray traced to intercepting geometry
2D ray tracing model in MatLab (E-beam bends in blue, photon ‘rays’ in green, strike points in red)

## Slide 11: Beam orbits and lattice functions
Example local phase space ellipses
Spatial extents:
Ellipse Equations:
APS-U lattice functions in the x and y plane
Spatial and angular beam deviation possibilities from local phase space ellipses in x,y planes
  Phase space ellipse extents calculated with Courant-Snyder lattice parameters
  APS-U physics provides parameters along finely spaced points across the sector
  Maximum beam extents limited by a limiting aperture or beam position limit detection system
Local ellipses discretized, large amounts of new ray paths with deviations tested in MatLab

## Slide 12: 3D numerical ray tracing geometry
Conical inline absorber
Crotch absorber
(v-style)
Inline absorber
(symmetric vertical planes)
End absorber (vertical plane)
Standard round tube
(cylinder)
Extrusion (round aperture + pumping slot)
Geometry programmed by cross section
  Round tubes
  Simplified extruded chambers with antechambers
  Photon absorbers (planar, conical, and v-shaped)
Photon extraction geometry not yet developed (future work!)
  Current program follows geometry along the main beam path

## Slide 13: 3D numerical ray tracing geometry
A:M1 Magnet
A:M2 Magnet
A Quad Doublet Section
A:M1 Magnet
A:M2 Magnet
B:M2 Magnet
B:M1 Magnet
BEAM
DIRECTION
Full scale 27.6 m length sector APS-U model built from sequential elements
Rays generated at points along colored paths representing the magnet lattice
Dipole paths in dark blue
Quadrupoles in light blue
Sextupoles in yellow

## Slide 14: Beam missteering: X and Y planes
1 missteered ray in x-plane
Full missteering from a local orbit in x-plane
Full missteering from a local orbit in both x and y-planes (green ray paths removed from image)

## Slide 15: 3D ray tracing results along length
Linear power across sector compared for ideal steering (green) and worst cases of missteering with a BPLD limit (red)
General nature of ray trace: spikes at compact absorber faces, high body loads on round chambers in FODO section, light body loads elsewhere
Ideal steering case has been verified to 2D ray trace and SynRad’s results

## Slide 16: 3D ray tracing results along length
Integrated results across individual chambers used for conservative boundary conditions for thermal/structural analysis
Typically ~10% higher loads than ideal case if a BPLD limit considered
Typical ANSYS thermal analysis of water-cooled APS-U chamber with inline absorber

## Slide 17: Informing BPLD limits
Permanent Magnet Insertion Device Vacuum Chamber:
Length: 5.322m
Straight section chambers with long, narrow, uncooled apertures
How to understand scraping possibilities and can a reasonable BPLD limit help minimize them?
Simplified model with ideal machining and alignment
Anticipate a full 200 mA BPLD limit of +/- 0.5 mm measured at a BPM (less constrained for beam current < 1 mA)
+/- 1.1 mm Y BPLD limit at A:P3 BPM *all rays pass through
+/- 1.2 mm Y BPLD limit at A:P3 BPM *reaches threshold for scraping from missteered rays
BEAM
DIRECTION

## Slide 18: Conclusions and future work
BEAM
DIRECTION
New MatLab program to investigate ray tracing with beam missteering
  Models built off of adjustable geometric parameters for system analysis and scenario studies
  Post-processed graphics help investigate results in 3D
  Results used for conservative heat loads in thermal analysis
Future work
  Current program suited for chambers along the beam path, will develop program for extracted rays
  Find efficient ways to model vacuum component misalignment
  Import geometry from 3D CAD

## Slide 19: Questions?